## Slide 1: Mathematical Models and AI for Theranostic Digital Twins
MODEL CATALOGUE · OCTOBER 2026
From virtual patients to virtual trials: every model behind the predictive engine, with equations, uses, status, and the best AI methods for building each layer
Hamid Abdollahi, PhD · Medical physics · quantitative imaging · AI · radiopharmaceutical therapy
Notes: This deck collects every mathematical model in my recent work: the DoseVLM dose-prediction code, the radiomics pipeline, the virtual-trials review and the research-vision talk. Part I explains each model with its equation and use. Part II recommends the best AI methods for building each layer of a digital twin. Status tags show whether a model is already in code, discussed in talks or the review, or proposed.

## Slide 2: Eight model layers make one predictive engine
EXECUTIVE SUMMARY
1 · Virtual patients
Who is in the trial: sampled cohorts, phantoms, growth
2 · Pharmacokinetics
Where the drug goes: PBPK ODEs, TACs, SUV
3 · Dosimetry
How much energy is absorbed: MIRD, voxel, EBRT
4 · Radiobiology
What dose does: LQ, BED with G factor, TCP, NTCP
5 · Updating and optimisation
Bayesian updates per cycle; choose activity
6 · Learned surrogates
DoseVLM: seconds instead of hours of simulation
7 · Imaging biomarkers
Radiomics: features, selection, classifiers
8 · Evaluation and credibility
AUC, calibration, gamma, V&V 40, trial statistics
Status of each model:
IN CODE
IN TALKS
IN REVIEW
PROPOSED
code = implemented in the repo · talks = research-vision slides · review = virtual-trials review · proposed = next step
Notes: The engine has eight layers. Layers 1 to 4 are the mechanistic chain from patient to biological effect. Layer 5 makes it a twin: it is updated with each patient's measurements and used to choose treatment. Layer 6 replaces slow simulations with learned surrogates. Layers 7 and 8 supply imaging inputs and prove the whole thing is credible.

## Slide 3: A virtual trial is a chain of models
HOW THE LAYERS CONNECT
PET / SPECT / CT
imaging input
Virtual cohort
θᵢ ~ p(θ | x)
PBPK kinetics
A(t) per organ
Voxel dosimetry
D = Ã ⊛ DVK
Radiobiology
BED, EQD2
TCP / NTCP
outcome
Decision
activity, cycles
Every cycle: post-therapy SPECT/PET → Bayesian update of patient parameters → re-plan the next cycle
Virtual trial
Run every arm (e.g. fixed 7.4 GBq vs model-guided activity) on the same virtual patients: a perfectly paired design.
Learned surrogates
Replace slow links (Monte Carlo dose, PBPK solves) with networks such as DoseVLM, so thousands of patients run in minutes.
Credibility
Step 1 technical fidelity · Step 2 external testing · Step 3 prospective evaluation, scaled to risk (ASME V&V 40).
Notes: Read the chain left to right. Images build the virtual patient; PBPK turns activity into time-activity curves; dosimetry turns those into absorbed dose; radiobiology turns dose into biological effect; TCP and NTCP turn effect into outcome probabilities; the decision layer picks activity and cycles. The amber loop is what makes it a digital twin rather than a one-off model: it is updated with each new measurement.

## Slide 4: The mathematical models, layer by layer
PART I
For each model: the equation, what each term means, where it is used, and whether it is already in code
Notes: Part I walks through the eight layers. Each slide gives the governing equation and a one-line explanation you can use when presenting or writing.

## Slide 5: Who is in the virtual trial
LAYER 1 · VIRTUAL PATIENTS
Parametric virtual population
IN TALKS
θᵢ ~ p(θ | xᵢ), xᵢ = (age, weight, eGFR, SUV, …)
Sample N = 1,000–10,000 patients from published covariate distributions. Use it to explore heterogeneity and enrich rare subgroups.
Mixed-effects (population) prior
IN TALKS
θᵢ = θ_pop · exp(ηᵢ), ηᵢ ~ N(0, Ω)
Typical value θ_pop plus log-normal between-patient variability Ω. It is also the prior for the per-patient Bayesian update (Layer 5).
Computational phantom
IN CODE
(x/a)² + (y/b)² ≤ 1; PTV: ‖(x − c)/r‖ ≤ 1
dosevlm/synthetic.py: random body, PTV ellipsoid, cord and parotids, random Rx and arcs. Known ground truth for testing the pipeline.
Mechanistic tumour growth
IN REVIEW
∂N/∂t = ∇·(D∇N) + k N (1 − N/θ) − R(D)
Reaction–diffusion: cell density N spreads (D) and grows logistically (k, capacity θ); R(D) kills cells. Calibrated to serial imaging.
Notes: Four ways to populate a virtual trial. The first two are statistical; the phantom is geometric and is already implemented for testing; the growth model adds time, so the twin can evolve between scans. In practice you combine them: sample parameters from the mixed-effects model, attach them to real or synthetic anatomy, and let tumours evolve.

## Slide 6: PBPK: where the radioligand goes
LAYER 2 · PHARMACOKINETICS
Per organ i (¹⁷⁷Lu-PSMA, Cancers 2024)
IN TALKS
Free ligand
Vᵢ dCᵢ/dt = Qᵢ (C_art − Cᵢ/Pᵢ) − k_on Rᵢ Cᵢ + k_off Bᵢ − λ_phys Cᵢ
Receptor-bound
dBᵢ/dt = k_on Rᵢ Cᵢ − (k_off + λ_int + λ_phys) Bᵢ
Internalised
dIᵢ/dt = λ_int Bᵢ − (λ_rel + λ_phys) Iᵢ
Free receptors
Rᵢ = R_tot,i − Bᵢ (hot + cold ligand share Rᵢ)
Kidney excretion
extra term − CL_R · C_art in the kidney balance
Parameters
Q: organ blood flow · P: tissue/blood partition
R_tot: receptor density (PSMA expression)
k_on, k_off: binding and unbinding rates
λ_int, λ_rel: internalisation and release
λ_phys = ln2 / 6.65 d for ¹⁷⁷Lu
CL_R: renal clearance (eGFR-linked)
Tumour sink effect. Large tumour burden binds more ligand, so less reaches kidneys and salivary glands. Only a mechanistic model with shared receptors predicts this.
Notes: PBPK is the core of the theranostic twin. Each organ has free, receptor-bound and internalised compartments, all decaying physically. Because hot and cold peptide compete for the same receptors, the model captures peptide amount effects and the tumour sink effect. Parameters come from literature plus patient imaging; patient-specific ones like receptor density are estimated from pre-therapy PET.

## Slide 7: Time–activity curves and integrated activity
LAYER 2 · FROM IMAGES TO ACTIVITY
SUV (body weight)
IN CODE
SUV = C · BW / (A_inj · e^(−λΔt))
Decay-corrected uptake per injected activity and body weight.
Time–activity fit
IN TALKS
A(t) = A₀ e^(−λ_eff t)
λ_eff = λ_phys + λ_bio, T_eff = ln2 / λ_eff
Mono- or bi-exponential fit to 3–4 scans over 4–7 days.
Time-integrated activity
IN TALKS
Ã = ∫₀^∞ A(t) dt = A₀ / λ_eff
1 time point: Ã ≈ A(t) · 2t / ln2
Hänscheid single-time-point estimate: one scan near t ≈ T_eff.
Chart: Illustrative ¹⁷⁷Lu-PSMA curves (% injected activity)
| 0 | 4 | 8 | 12 | 16 | 20 | 24 | 28 | 32 | 36 | 40 | 44 | 48 | 52 | 56 | 60 | 64 | 68 | 72 | 76 | 80 | 84 | 88 | 92 | 96 | 100 | 104 | 108 | 112 | 116 | 120 | 124 | 128 | 132 | 136 | 140 | 144 | 148 | 152 | 156 | 160 | 164 | 168
Kidney (T_eff 35 h) | 4 | 3.695 | 3.414 | 3.154 | 2.914 | 2.692 | 2.487 | 2.297 | 2.122 | 1.961 | 1.811 | 1.673 | 1.546 | 1.428 | 1.32 | 1.219 | 1.126 | 1.04 | 0.961 | 0.888 | 0.82 | 0.758 | 0.7 | 0.647 | 0.598 | 0.552 | 0.51 | 0.471 | 0.435 | 0.402 | 0.371 | 0.343 | 0.317 | 0.293 | 0.271 | 0.25 | 0.231 | 0.213 | 0.197 | 0.182 | 0.168 | 0.155 | 0.144
Tumour (T_eff 70 h) | 3 | 2.883 | 2.772 | 2.664 | 2.56 | 2.461 | 2.365 | 2.274 | 2.185 | 2.1 | 2.019 | 1.94 | 1.865 | 1.793 | 1.723 | 1.656 | 1.592 | 1.53 | 1.471 | 1.413 | 1.359 | 1.306 | 1.255 | 1.206 | 1.16 | 1.114 | 1.071 | 1.03 | 0.99 | 0.951 | 0.914 | 0.879 | 0.845 | 0.812 | 0.78 | 0.75 | 0.721 | 0.693 | 0.666 | 0.64 | 0.615 | 0.591 | 0.568
Area under each curve = Ã. Longer tumour retention gives tumour more dose per GBq than kidney.
Notes: Imaging gives activity at a few time points. Fitting an exponential gives the effective half-life, and the area under the curve is the time-integrated activity, the quantity dosimetry needs. The single-time-point method is a practical shortcut when only one post-therapy scan is available. The curves are illustrative, not patient data.

## Slide 8: From integrated activity to absorbed dose
LAYER 3 · DOSIMETRY
MIRD organ dosimetry
IN TALKS
D(r_T) = Σ_S Ã(r_S) · S(r_T ← r_S)
S-values give dose to target per decay in source, from reference phantoms. Fast, but organ-level only and assumes uniform uptake.
Voxel dosimetry (DVK)
IN TALKS
D(v) = (Ã ⊛ DVK)(v)
Convolve the voxel Ã map with a dose-voxel kernel. Captures heterogeneity; assumes homogeneous tissue around each voxel.
Local energy deposition
IN TALKS
D(v) = Ã(v) · Ē / m(v)
For β emitters whose range is below the voxel size (¹⁷⁷Lu): all energy stays in the voxel. Simple and surprisingly accurate.
Monte Carlo and AI surrogates
IN TALKS
D = MC(Ã, ρ_CT) ≈ f_θ(Ã, CT)
Monte Carlo (e.g. GATE) is the reference but takes hours; a trained network f_θ approximates it in about 3 s (Layer 6).
Notes: Four levels of dosimetry, from organ-level MIRD to full Monte Carlo. The trade-off is accuracy against time. For a twin that must run thousands of virtual patients, AI surrogates trained on Monte Carlo give near-reference accuracy in seconds.

## Slide 9: Beam physics and dose metrics in DoseVLM
LAYER 3 · EXTERNAL-BEAM GEOMETRY AND PLAN QUALITY
Divergent fluence projection
IN CODE
Φ(v) = Σ_seg MU · 𝟙[v ∈ aperture] · (SAD / (SAD − z))²
IEC 61217 couch, gantry and collimator rotations; jaw + MLC aperture test; inverse-square weight (rtplan.py).
Pencil-beam dose (synthetic)
IN CODE
D = G_σ ⊛ (Φ · e^(−μ d)), μ = 0.004 mm⁻¹
Exponential attenuation with depth d plus Gaussian scatter blur. Used only to make learnable synthetic data.
Dose–volume histogram metrics
IN CODE
D_x = dose to hottest x %; V_x = % volume ≥ x Gy
PTV: D99, D95, D1, Dmean. OAR: Dmean, D0.1cc (metrics.py and the plain-Python dvh_tool.py).
3-D gamma index
IN CODE
γ = min_r′ √( ΔD²/(δ·D_max)² + |r′ − r|²/DTA² )
A voxel passes if γ ≤ 1 at 3 % / 3 mm with a 10 % low-dose threshold. Pass rate compares predicted with clinical dose.
Notes: These are the external-beam models already implemented in DoseVLM. The fluence projection gives the network explicit beam geometry. DVH metrics and gamma are the clinical yardsticks for whether a predicted dose matches the real one.

## Slide 10: From physical dose to biological effect
LAYER 4 · RADIOBIOLOGY
Linear-quadratic survival
IN TALKS
S = exp(−αD − βD²)
Fraction of cells surviving dose D. α/β sets fractionation sensitivity: low for late-responding tissue and prostate.
BED for external beam
IN TALKS
BED = n d (1 + d / (α/β))
n fractions of d Gy. Lets different schedules be compared on one biological scale.
BED for RPT (dose-rate G factor)
IN TALKS
BED = D (1 + G · D / (α/β))
G = λ_eff / (λ_eff + μ)
Continuous, decaying dose rate allows repair (rate μ). Example kidney: T_eff 30 h, T_rep 2.8 h → G ≈ 0.085.
EQD2
IN TALKS
EQD2 = BED / (1 + 2 / (α/β))
Dose in 2 Gy fractions with the same effect, so RPT and external-beam limits can be added and compared.
Notes: Radiobiology converts absorbed dose to effect. The key RPT-specific idea is the G factor: because dose is delivered slowly and decays, cells repair during irradiation, so the quadratic term shrinks. This is the subject of my IEEE TRPMS 2025 paper. Parameter values here are illustrative.

## Slide 11: TCP and NTCP define the therapeutic window
LAYER 4 · OUTCOME PROBABILITY
Tumour control (Poisson)
IN TALKS
TCP = exp(−N₀ · e^(−α · BED))
N₀ = ρ · V clonogens
Probability that no clonogenic cell survives. Steep sigmoid in BED.
Normal-tissue complication (LKB)
IN REVIEW
NTCP = Φ((gEUD − TD₅₀) / (m · TD₅₀))
gEUD = (Σ vᵢ Dᵢ^(1/n))ⁿ
n = volume effect (n → 1 parallel, n → 0 serial organ); m = slope.
Chart: Illustrative curves vs BED (Gy)
| 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100 | 105 | 110 | 115 | 120
TCP (tumour) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.001 | 0.045 | 0.231 | 0.5 | 0.721 | 0.857 | 0.93 | 0.966 | 0.984 | 0.992 | 0.996 | 0.998 | 0.999 | 1 | 1 | 1
NTCP (organ at risk) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.001 | 0.003 | 0.006 | 0.013 | 0.026 | 0.048 | 0.082 | 0.133 | 0.202 | 0.289 | 0.391 | 0.5 | 0.609 | 0.711 | 0.798 | 0.867 | 0.918 | 0.952
Parameters illustrative: TCP₅₀ = 60 Gy, α = 0.15 Gy⁻¹; TD₅₀ = 90 Gy, m = 0.2. The gap between curves is the window a twin tries to exploit per patient.
Notes: TCP and NTCP turn biological dose into probabilities of cure and of harm. Their separation is the therapeutic window. A twin shifts both curves per patient, using that patient's kinetics and anatomy, which is why fixed activity can under-treat one patient and harm another.

## Slide 12: Learn each patient, then choose the treatment
LAYER 5 · TWIN UPDATING AND OPTIMISATION
Bayesian update across cycles
IN TALKS
p(θ | y₁…ₖ) ∝ p(yₖ | θ) · p(θ | y₁…ₖ₋₁)
θ̂_MAP = argmax_θ p(θ | y)
Population prior + sparse post-therapy SPECT. The prediction band narrows from cycle 1 to cycle 2.
Activity optimisation
IN TALKS
A* = max A s.t. BED_OAR(A) ≤ L
linear case: A* = A_ref · D_lim / D(A_ref)
e.g. kidney limit. Tumour sink and saturation make D(A) nonlinear, so the PBPK twin is needed.
Illustrative ¹⁷⁷Lu-PSMA twin: activity alone changes the outcome
7.4 GBq
Organs safe · tumour refractory
8.3 GBq
Organs safe · tumour responds
10 GBq
Tumour responds · organ toxicity
Design space to optimise: activity, number of cycles, interval, bolus vs metronomic infusion, hot/cold ligand ratio. Objective: maximise tumour BED subject to every OAR limit.
Notes: This layer is what makes a model a digital twin. After each cycle the patient's parameters are re-estimated from new measurements, and the next cycle is optimised. The three activities are from my research-vision talk, after Yazdani et al. 2026, and are illustrative, not recommendations.

## Slide 13: DoseVLM: a vision-language dose engine
LAYER 6 · LEARNED SURROGATE
CT + masks + beam projection
3-D residual U-Net encoder
Cross-attention to plan tokens
Decoder + FiLM
Dose / Rx (softplus)
Plan text + control-point tokens (gantry sin/cos, MU, MLC area) → plan transformer
Attention and conditioning
IN CODE
Attn(Q,K,V) = softmax(QKᵀ / √d) V
FiLM: f′ = f (1 + γ(z)) + β(z)
Voxels (Q) query plan tokens (K, V); pooled plan embedding z rescales decoder features.
Training loss
IN CODE
L = MAE_body + MAE_PTV + 0.5 L_DVH + 0.1 L_∇
L_DVH = mean |sort(ŷ) − sort(y)| = W₁
Sorted-dose L1 equals the Wasserstein-1 distance between DVHs; gradient term keeps penumbra sharp.
Output in Gy: D̂ = softplus(h) · Rx · 𝟙_body · AdamW, cosine learning rate with warm-up, 96³ PTV-focused crops
Notes: DoseVLM is the working example of a learned surrogate in my repo. It predicts 3-D VMAT dose from CT, structures and the plan, reading the plan both as images and as text. In a virtual trial you change the plan text or arcs and re-predict dose in seconds. It is research use only.

## Slide 14: Radiomics: from image to robust features
LAYER 7 · IMAGING BIOMARKERS (1/2)
IBSI discretisation
IN CODE
bin(x) = ⌊x / w⌋ − ⌊min / w⌋ + 1
Fixed bin width w = 25 HU for CT, or fixed bin count 32 for MR and PET. Makes texture comparable across patients.
First-order and texture
IN CODE
H = −Σ p(i) log₂ p(i)
GLCM contrast = Σ (i − j)² p(i, j)
Plus shape, GLRLM, GLSZM, GLDM, NGTDM; on original, LoG and wavelet images.
Robustness filter ICC(3,1)
IN CODE
ICC = (MS_R − MS_E) / (MS_R + (k − 1) MS_E)
Erode and dilate the mask by one voxel; keep only features with ICC ≥ 0.75.
Registration (mutual information)
IN CODE
I(F;M) = Σ p(f,m) log [ p(f,m) / (p(f) p(m)) ]
Rigid → affine → B-spline, maximising Mattes MI, when a mask was drawn on another image (e.g. T2 → ADC).
Notes: Radiomics supplies imaging inputs to the twin, such as heterogeneity and endocrine-organ signatures. Before modelling, features are standardised by IBSI discretisation and filtered for robustness so that small contouring changes do not drive the result.

## Slide 15: Selection and classifiers without data leakage
LAYER 7 · IMAGING BIOMARKERS (2/2)
mRMR and LASSO selection
IN CODE
mRMR: max_f [ I(f; y) − mean_{s∈S} I(f; s) ]
LASSO: min_β ℓ(y, Xβ) + λ‖β‖₁
Also Mann–Whitney with BH-FDR, ReliefF, Boruta, RFE. All fitted inside each CV fold.
Classifiers
IN CODE
Logistic: p = σ(βᵀx) = 1 / (1 + e^(−βᵀx))
Ensembles: RF, XGBoost, LightGBM, SVM, MLP
Soft-voting ensemble of the top 3 by nested-CV AUC.
Class imbalance (SMOTE)
IN CODE
x_new = xᵢ + u (x_nn − xᵢ), u ~ U(0, 1)
Synthetic minority samples along lines to nearest neighbours; or class weights, ADASYN, under-sampling.
Nested CV + Bayesian tuning
IN CODE
TPE: choose x maximising l(x) / g(x)
Outer folds score, inner folds tune (Optuna). Threshold picked on out-of-fold data; test set used once.
Worked example: endocrine-organ radiomics in PSMA-negative recurrence (n = 101): PET + CT + clinical AUC 0.758 vs 0.727 clinical alone (gain not significant)
Notes: Every step that sees labels lives inside one pipeline that is refitted in each fold, so no information leaks from test to training. The PSMA-negative endocrine study is the applied example.

## Slide 16: Is the prediction right, calibrated and useful?
LAYER 8 · EVALUATION
Discrimination
IN CODE
AUC = P(s⁺ > s⁻) = U / (n⁺ n⁻)
Youden J = Se + Sp − 1
DeLong test and bootstrap 95 % CI; PR-AUC, MCC, Cohen's κ, LR±.
Calibration
IN CODE
Brier = mean (p − y)²
ECE = Σ_b (n_b / N) |acc_b − conf_b|
Plus calibration slope and intercept and Hosmer–Lemeshow.
Clinical usefulness
IN CODE
NB(p_t) = TP/N − (FP/N) · p_t / (1 − p_t)
Decision-curve analysis: net benefit across threshold probabilities vs treat-all and treat-none.
Explainability
IN CODE
f(x) = φ₀ + Σⱼ φⱼ (Shapley values)
SHAP attributes each prediction to features; permutation importance checks the ranking.
Notes: Three questions: does the model separate classes (AUC), are its probabilities honest (calibration), and does using it beat simple strategies (net benefit). Calibration matters most for a twin, because its probabilities feed decisions.

## Slide 17: When can a virtual trial be trusted?
LAYER 8 · CREDIBILITY AND TRIAL STATISTICS
Paired arm comparison
IN REVIEW
Δᵢ = Yᵢ(arm B) − Yᵢ(arm A), same virtual patient i
Every patient gets every arm, so between-patient noise cancels; far fewer subjects are needed.
Sample size for paired design
PROPOSED
n = ((z₁₋α/₂ + z₁₋β) · σ_Δ / δ)²
δ = smallest difference worth detecting; σ_Δ = SD of paired differences.
Uncertainty propagation
IN REVIEW
Y⁽ᵏ⁾ = g(θ⁽ᵏ⁾), θ⁽ᵏ⁾ ~ p(θ | data), k = 1…K
Monte Carlo through the whole chain: phantom → kinetics → dose → NTCP. Report endpoint intervals, not points.
Risk-informed credibility
IN REVIEW
required evidence ∝ model influence × decision consequence
ASME V&V 40 and FDA 2023 guidance. Validate dose first, then response; agree with a real trial before extrapolating.
Notes: A virtual trial is only as trustworthy as its weakest model. Paired designs make virtual trials statistically efficient. Uncertainty must be propagated end to end. The V&V 40 framework scales the validation effort to how much the decision depends on the model.

## Slide 18: Best AI models for digital-twin development
PART II
Which AI family to use for each twin layer, why it fits, its caveats, and the open-source tools to start with
Notes: Part II is a practical guide. There is no single best AI model for digital twins. The best choice depends on the layer, how much mechanism you know, and how much data you have.

## Slide 19: Pick AI by mechanism knowledge and data size
CHOOSING A METHOD
Strong mechanism · small data
Bayesian PBPK, PINNs, universal differential equations
Most theranostic twins today: physics known, few scans per patient.
Strong mechanism · large data
Neural operators (FNO, DeepONet), MC emulators
Learn the simulator itself: Monte Carlo dose, PBPK solves in milliseconds.
Weak mechanism · small data
Gaussian processes, TabPFN, regularised regression
Biomarkers and outcomes in cohorts of 50–500 patients.
Weak mechanism · large data
Deep nets, foundation models, diffusion models
Segmentation, denoising, synthetic anatomy, multimodal fusion.
MECHANISM
DATA SIZE →
Notes: Top row: you know the physics or physiology. Bottom row: you do not. Left column: little data per patient or few patients. Right column: lots of data or a simulator that can generate it. Theranostic twins mostly start top-left and use the top-right to accelerate.

## Slide 20: Best AI families for each twin layer
OVERVIEW
Twin layer | Best AI models | Starter tools
Imaging: denoise, reconstruct | U-Net / ResUNet, conditional GAN, diffusion denoisers | MONAI, PyTorch
Segmentation | nnU-Net, TotalSegmentator, MedSAM / SAM-2 style promptable | nnU-Net, MONAI Auto3DSeg
Kinetics (PBPK) | PINNs, neural ODEs, universal differential equations | torchdiffeq, DeepXDE, Julia SciML
Dosimetry | CNN / Swin-UNETR voxel dose, neural operators, DoseVLM | MONAI, neuraloperator, OpenGATE
Virtual patients | 3-D latent diffusion (MAISI), GAN / VAE; copulas, CTGAN | MONAI generative, SDV
Calibration and UQ | Simulation-based inference, hierarchical Bayes, conformal | sbi, PyMC / Stan, MAPIE
Outcome | Cox, random survival forest, DeepSurv, XGBoost, TabPFN | lifelines, scikit-survival
Decision | Bayesian optimisation, reinforcement learning, MPC | BoTorch, Optuna, Gymnasium
Orchestration | Frontier LLM coding agents, biomedical text encoders | Claude Code, BiomedBERT
Notes: One row per twin layer. The next slides go through each family in detail: what it is, how it works mathematically, where it fits in a theranostic twin, and its main caveat.

## Slide 21: Hybrid physics + AI: the core of a twin
AI FAMILY 1 · SCIENTIFIC MACHINE LEARNING
PINN
L = L_data + λ ‖𝒩[u_θ]‖²
Fit PBPK or diffusion to sparse SPECT; physics fills gaps. Caveat: stiff ODEs train poorly.
Neural ODE
dz/dt = f_θ(z, t)
Learn kinetics from irregular time points. Caveat: less interpretable than PBPK.
Universal DE
dx/dt = f_PBPK(x; θ) + NN_φ(x)
Keep known PBPK, learn only the missing term (e.g. sink saturation). Best fit for theranostics.
Neural operator
𝒢_θ : Ã(·) ↦ D(·) (FNO, DeepONet)
Learn the whole Monte Carlo map; resolution-independent dose in milliseconds.
GP emulator
y ~ GP(m(x), k(x, x′))
Surrogate with error bars from ~100 simulator runs; Sobol sensitivity and calibration.
Recommended first build: a universal differential equation around the ¹⁷⁷Lu-PSMA PBPK model, calibrated with simulation-based inference.
Notes: Scientific machine learning keeps the physics and lets a network learn what the physics misses. For theranostics, a universal differential equation is the most natural fit: the PBPK structure stays interpretable, and the network learns only a correction term. Neural operators are the best way to replace Monte Carlo dosimetry once enough simulations exist.

## Slide 22: Reliable inputs: segmentation and low-count imaging
AI FAMILY 2 · IMAGING AI
nnU-Net
self-configuring 3-D U-Net: patch, spacing, augmentation
Strongest out-of-the-box baseline for organ and lesion segmentation. Train per task; still the benchmark to beat.
TotalSegmentator
pre-trained: 100+ CT structures (MR version too)
Instant organs at risk for dosimetry (kidneys, salivary glands, liver, marrow). Check small organs by eye.
MedSAM / promptable models
mask = f(image, box or point prompt)
Foundation models for interactive lesion contouring; fast QA and correction. Weaker on PET/SPECT without fine-tuning.
Low-count SPECT/PET denoising
x̂ = f_θ(x_low) (U-Net, cGAN, diffusion)
Can cut ¹⁷⁷Lu SPECT time by 50–75 %. Always measure activity bias and small-lesion recovery on phantoms.
Notes: Garbage in, garbage out: the twin is only as good as its activity maps and contours. nnU-Net and TotalSegmentator give reliable contours; promptable foundation models speed up correction. AI denoising shortens scans, but must preserve quantitative accuracy, which is the point of my Aim 2.

## Slide 23: Fast dose engines and synthetic cohorts
AI FAMILY 3 · DOSIMETRY AND VIRTUAL PATIENTS
Deep voxel dosimetry
D̂ = f_θ(SPECT/PET activity, CT density)
U-Net or Swin-UNETR trained on Monte Carlo; learned dose-voxel kernels. Seconds per patient instead of hours.
Dose prediction for planning
D̂ = f_θ(CT, masks, plan) (DoseVLM)
OpenKBP-style cascaded U-Nets, diffusion dose models, and vision-language DoseVLM for external beam.
3-D generative anatomy
x₀ ← denoise(x_T), conditioned on masks
Latent diffusion (e.g. MONAI MAISI) makes CT with organ labels; GANs are fast but can mode-collapse.
Tabular virtual covariates
(age, eGFR, PSA, SUV) ~ copula / CTGAN
Sample realistic joint covariates. Validate with MMD, downstream fidelity and membership-inference privacy tests.
Notes: Dosimetry AI removes the Monte Carlo bottleneck. Generative models scale the cohort, but realism must be shown, not assumed: compare distributions, check that downstream predictions behave the same, and test privacy.

## Slide 24: Calibrate the twin, then act on it safely
AI FAMILY 4 · INFERENCE, UNCERTAINTY AND DECISIONS
Simulation-based inference
q_φ(θ | y) ≈ p(θ | y), trained on (θ, y) ~ sim
Neural posterior estimation gives each patient's PBPK posterior in milliseconds once trained (sbi package).
Conformal prediction
P(y ∈ C(x)) ≥ 1 − α
Distribution-free intervals around any model (dose, NTCP). Also deep ensembles and MC dropout for UQ.
Bayesian optimisation
x_next = argmax EI(x) on a GP surrogate
Search activity, cycles and interval with few expensive twin runs (BoTorch, Optuna).
Reinforcement learning / MPC
π* = argmax E[Σ rₜ], r = BED_T − penalty(OAR)
Cycle-by-cycle adaptation as a sequential decision. Train only in silico; keep a clinician in the loop.
Notes: These methods turn a predictive model into a decision tool. Simulation-based inference makes per-patient calibration instant. Conformal prediction gives honest uncertainty. Bayesian optimisation and reinforcement learning search the design space, but any recommendation stays decision support with explicit uncertainty.

## Slide 25: Predict outcomes and accelerate the work
AI FAMILY 5 · OUTCOME MODELS AND FOUNDATION MODELS
Survival models
h(t | x) = h₀(t) · exp(βᵀx)
Cox for interpretability; random survival forests and DeepSurv for nonlinearity. Report C-index and calibration.
Small-data tabular
TabPFN, XGBoost / LightGBM, penalised LR
TabPFN is a pre-trained transformer that is often strongest on small tables. Always compare against logistic regression.
Multimodal fusion
z = fuse(PET, CT, dose, clinical, text)
Cross-attention fusion of image, dose and record, as in DoseVLM. Needs larger multi-site data.
LLMs and coding agents
Claude, other frontier LLMs; BiomedBERT, BiomedCLIP
Write and test pipelines, map literature (e.g. the 73-report evidence map), draft protocols. Not for unsupervised clinical decisions.
Notes: For outcomes, start simple and earn complexity: Cox and logistic baselines first, then tree ensembles and TabPFN, then multimodal deep fusion when data allow. Large language models are best used as engineering and research accelerators, as I did to build DoseVLM and the radiomics pipeline, with every output verified.

## Slide 26: Best AI choice for each research aim
RECOMMENDED STACK
1
Imaging biomarkers
PyRadiomics + nested CV; logistic, XGBoost, TabPFN; SHAP
2
AI-enhanced imaging
nnU-Net / TotalSegmentator; U-Net or diffusion denoising with quantitative checks
3
Digital twins
UDE around PBPK + simulation-based inference; neural-operator dose emulator
4
Therapy integration
DoseVLM for external beam + RPT voxel dose; Bayesian optimisation of activity
5
Virtual trials
Copula / diffusion cohorts, GP emulators, conformal UQ, paired-design statistics
Shared layer for all aims: MONAI + PyTorch, version-controlled pipelines, and V&V 40-style validation gates.
Notes: This maps Part II onto the five aims of my research program. Each aim gets a concrete, open-source starting point.

## Slide 27: Mechanism first, AI to scale, validation throughout
TAKEAWAYS AND NEXT STEPS
Already in code: dose physics, DVH, gamma, DoseVLM, radiomics and evaluation.
Next: a PBPK + BED module beside DoseVLM, then TCP/NTCP to turn dose into outcome.
Then: uncertainty propagated end to end, and a pilot virtual trial of fixed vs model-guided activity.
Notes: Close with the three messages. Much of the stack already exists. The missing pieces are the kinetic and radiobiological layers, uncertainty propagation and a first pilot virtual trial.

## Slide 28: Sources for the models and AI methods
KEY REFERENCES
Abdollahi H et al. Theranostic digital twins. Theranostics 2024;14:3404–22
Abdollahi H et al. PBPK in ¹⁷⁷Lu-PSMA therapy. Cancers 2024;16:3120
Abdollahi H et al. Low-dose-rate radiobiology in RPT. IEEE TRPMS 2025;9:843–56
Abadi E et al. Virtual clinical trials in medical imaging. J Med Imaging 2020
Badano A et al. VICTRE in silico trial. JAMA Netw Open 2018
Langendijk JA et al. Model-based proton selection. Radiother Oncol 2013
Viceconti M et al. VV&UQ for in silico trials. Methods 2021
Babier A et al. OpenKBP. Med Phys 2021
Hänscheid H et al. Single-time-point dosimetry. J Nucl Med 2018
Isensee F et al. nnU-Net. Nat Methods 2021
Wasserthal J et al. TotalSegmentator. Radiol AI 2023
Ma J et al. MedSAM. Nat Commun 2024
Raissi M et al. Physics-informed neural networks. J Comput Phys 2019
Chen RTQ et al. Neural ODEs. NeurIPS 2018
Rackauckas C et al. Universal differential equations. arXiv 2020
Li Z et al. Fourier neural operator. ICLR 2021
Cranmer K et al. Simulation-based inference. PNAS 2020
Hollmann N et al. TabPFN. Nature 2025
Compiled from memory and from the repo review; verify volume and page numbers before formal citation.
Notes: Key references for each model and AI family. Check bibliographic details before citing.